## Slide 1: Things you need for the circuit
Android Things Compatible Board (one of the following boards)
  Raspberry Pi 3 board
  NXP Pico i.MX7D board
Pimoroni Rainbow HAT for Android Things (Rainbow HAT has a built in temperature sensor)

## Slide 2: Flash the Android Things Image to your board
For example :
NXP Pico i.MX7D Flash Image from https://developer.android.com/things/hardware/imx7d.html
Raspberry Pi 3 Flash Image from https://developer.android.com/things/hardware/raspberrypi.html

## Slide 3: Prepare your Android Things Board (2)
Make sure your board is connected to wifi.
If not:
  am startservice -n com.google.wifisetup/.WifiSetupService -a WifiSetupService.Connect -e ssid <your wifi network> -e passphrase <your wifi password>

## Slide 4: Connect the Rainbow HAT to the Android Things board
NXP i.MX7D board is used in this example

## Slide 5: Prepare your Android Things Board for MIT App Inventor
Install the Android Things App Inventor Companion on your board
Android Things App Inventor Companion is available from:
  https://github.com/thilankam/androidthings-appinventor-companion

## Slide 6: Run the Android Things App Inventor Companion on your board

## Slide 7: You should see something similar to the following on our console.
Make a note of these values as these will be needed when configuring your MIT App Inventor app.

## Slide 8: Prepare Your App Inventor Instance
Download the Android Things extension from:
http://thilankam.github.io/android-things
Upload the extension to your project

## Slide 9: Create a sample project with Labels, Textboxes and a Button.
We will be using two Textboxes to get input values for temperature thresholds and a button to start monitoring current temperature .

## Slide 10: Configure the Android Things Components.

## Slide 11: AndroidThingsBoard
“Initialize” method has to be called with the parameters given by your board in a previous step.
  “identifier”: uniquely matches the messages sent to your board.
  “hardwarePlatform”: the board type
  “messagingHost” : the MQTT server address
  “messagingPort” : the MQTT server port

## Slide 12: AndroidThingsTemperatureSensor
“Register” method has to be called before any target events or callbacks.

## Slide 13: Buttons / Textboxes
“Monitor Temperature” Button Click  AndroidThingsTemperatureSensor.monitor will start monitoring the current temperature.
Hot Threshold Textbox will intake the input value from user.
Cold Threshold Textbox will intake the input value from user.

## Slide 14: Complete App Inventor Program

## Slide 15: Demo