## Slide 1: What is AndroidThingsPWM?
A component that can be used to change the following values of a PWM device attached to an Android Things board:
  PWM Enabled
  PWM Frequency
  PWM Duty Cycle

## Slide 2: Tutorial Goal
In this tutorial we will see how we can change the PWM values programmatically to create a mini water sprinkler.

## Slide 3: Things you need for the circuit
Android Things Compatible Board (one of the following boards)
  Raspberry Pi 3
  NXP Pico i.MX7D, Argon etc.
1 Stepper Motor
3 Jumper Wires
1 Breadboard

## Slide 4: Connect the Circuit

## Slide 5: Prepare your Android Things Board (1)
One time setup ONLY (if not done already).
Flash the Android Things Image to your board. For example:
  Download and Install NXP Pico i.MX7D Flash Image from: https://developer.android.com/things/hardware/imx7d.html
  Download and Install Raspberry Pi 3 Flash Image from: https://developer.android.com/things/hardware/raspberrypi.html

## Slide 6: Prepare your Android Things Board (2)
Install the Android Things App Inventor Companion available from:
  https://github.com/thilankam/androidthings-appinventor-companion

## Slide 7: Prepare your Android Things Board (3)
Make sure your board is connected to wifi.
If not:
  am startservice -n com.google.wifisetup/.WifiSetupService -a WifiSetupService.Connect -e ssid <your wifi network> -e passphrase <your wifi password>

## Slide 8: Run the Android Things App Inventor Companion on your board

## Slide 9: You should see something similar to the following on your console.
Make a note of these values as these will be needed when configuring your MIT App Inventor app.

## Slide 10: Prepare Your App Inventor Instance
Download the Android Things extension from:
http://thilankam.github.io/android-things
Upload the extension to your project.

## Slide 11: Create an App Inventor project
“Run Sprinkler” button:
  Change the DutyCycle of the AndroidThingsPWM Component.
  This specific program changes the DutyCycle value in a loop to emulate a ‘sprinkler’ system.
  Changes in the sprinkler’s direction is also calculated.
AndroidThingsPWM:
  Component that models an Android Things PWM device.

## Slide 12: Configure the Android Things Components.

## Slide 13: Initialize AndroidThingsBoard
“Initialize” method has to be called with the parameters given by your board in a previous step.
  “identifier”: uniquely matches the messages sent to your board.
  “hardwarePlatform”: the board type
  “messagingHost” : the MQTT server address
  “messagingPort” : the MQTT server port

## Slide 14: Register AndroidThingsPWM
“Register” method has to be called before any target events or callbacks.
  “pwmName” : the name of the pin as designated as the PWM port in the PinOut diagram for your Android Things compatible board.
  “androidThingsBoard” : the board that this pin is part of.

## Slide 15: Initialize Global Variables
Here are some of the global variables used in the program.

## Slide 16: Create the Delay Procedure
This procedure ‘sleeps’ for a small predetermined period of time.

## Slide 17: Button Click
Run the stepper motor like a mini water sprinkler.
The direction of the motor and the duty cycle is changed in a loop.
The delay procedure is called in each iteration of the loop.

## Slide 18: Complete App Inventor Program

## Slide 19: Demo