## Slide 1: Things you need for the circuit
Android Things Compatible Board
  Raspberry Pi 3
  NXP Pico, Argon etc.
1 LED
1 Resistor
2 Jumper Wires
1 Breadboard

## Slide 2: Connect the circuit

## Slide 3: On either an Edison board

## Slide 4: Or on the Raspberry Pi 3 board

## Slide 5: Prepare your Android Things Board (1)
Install the Android Things App Inventor Companion available from:
  https://github.com/thilankam/androidthings-appinventor-companion

## Slide 6: Prepare your Android Things Board (2)
Make sure your board is connected to wifi.
If not:
  am startservice -n com.google.wifisetup/.WifiSetupService -a WifiSetupService.Connect -e ssid <your wifi network> -e passphrase <your wifi password>

## Slide 7: Run the Android Things App Inventor Companion on your board

## Slide 8: You should see something similar to the following on our console.
Make a note of these values as these will be needed when configuring your MIT App Inventor app.

## Slide 9: Prepare Your App Inventor Instance
Download the Android Things extension from:
http://thilankam.github.io/android-things
Upload the extension to your project

## Slide 10: Create a sample project with On and Off Buttons.
We will be using these buttons to control the LED in our circuit.

## Slide 11: Configure the Android Things Components.

## Slide 12: AndroidThingsBoard
“Initialize” method has to be called with the parameters given by your board in a previous step.
  “identifier”: uniquely matches the messages sent to your board.
  “hardwarePlatform”: the board type
  “messagingHost” : the MQTT server address
  “messagingPort” : the MQTT server port

## Slide 13: AndroidThingsGPIO
“Register” method has to be called before any target events or callbacks.
  “pinName” : the name of the pin as designated in the PinOut diagram for your Android Things compatible board.
  “isOutput” : the directionality of the pin, i.e. true indicates an output device such as an LED is attached.
  “androidThingsBoard” : the board that this pin is part of.

## Slide 14: Buttons
“On” Click  Pin state true (turn LED on)
“Off” Click  Pin state false (turn LED off)

## Slide 15: Complete App Inventor Program

## Slide 16: Demo